## Slide 1
BOOT_SEQUENCE_INIT..
01
REAL_TIME_KERNEL
FreeRTOS
Hands-on Workshop using ESP32
FREE_RTOS v10.x
ESP32 @ 240MHz
SYSTEM READY
Notes: Explain: Open like a system booting up. Explain that students will move from simple sketches to a real multitasking firmware design.
Analogy: A laptop boot screen: first the hardware wakes up, then services start.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: Who has used delay() to make an LED blink?
Common mistake: Do not promise that RTOS makes code automatically faster; it makes behavior structured and predictable.
Animation suggestion: Fade in the boot log after the title.
Transition suggestion: Move from title to why this matters.

## Slide 2
INTRO
02
This workshop turns sketches into firmware
Students start with blink and end with a coordinated real-time system.
Start simple
GPIO, Serial, millis, cores
Add structure
Tasks, scheduler, timing
Coordinate
Queues, semaphores, mutex
Integrate
Timers, ISR, notifications
Notes: Explain: Set the learning promise: every topic helps the final system become less fragile.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Preview the final project so the path has a destination.

## Slide 3
INTRO
03
The final project is the north star
A live ESP32 app with sensors, display, alerts, controls, and emergency response.
01
Inputs
02
Tasks
03
Queue
04
LCD
05
Alert
Notes: Explain: Show the destination before the details. Students should know why each concept exists.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: Which parts must run at the same time?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Now map the two workshop days.

## Slide 4
INTRO
04
Two days, one firmware story
Setup
Board + IDE
Refresher
Arduino basics
RTOS
Tasks + schedule
IPC
Queues + semaphores
System
Timers + ISR + final
Notes: Explain: Use the handwritten schedule as the pacing guide without putting exact times on screen.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Ground the story in the physical kit.

## Slide 5
INTRO
05
Every team gets a small embedded lab
The kit is enough to model real products without hiding the firmware.
ESP32
GPIO
ADC
I2C
PWM
UART
CPU0
CPU1
I2C LCD for shared output
Buttons for events and interrupts
Potentiometers for changing inputs
LEDs and buzzer for feedback
Notes: Explain: Introduce the hardware as the workshop's vocabulary.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: Which devices are inputs and which are outputs?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Before RTOS, confirm the basic Arduino vocabulary.

## Slide 6
INTRO
06
Setup is part of the system
IDE
Arduino IDE installed with ESP32 board package
Board
Correct COM port, upload speed, and boot button workflow
Libraries
LCD library and FreeRTOS examples ready
Teams
2-3 students share one kit and one debugging log
Notes: Explain: The handwritten plan starts with setup. Treat it as risk reduction, not admin.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Move into the refresher module.

## Slide 7
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
07
MODULE 00
ESP32 and Arduino Refresher
// make the board obey before asking it to multitask
NEXT_MODULE
Notes: Explain: Use this as a clean reset before ESP32 and Arduino Refresher. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 8
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
08
The ESP32 is not just an Arduino with Wi-Fi
It has two cores, many peripherals, and a real FreeRTOS runtime underneath.
ESP32
GPIO
ADC
I2C
PWM
UART
CPU0
CPU1
Two Xtensa cores
GPIO, ADC, PWM, I2C, UART
FreeRTOS already runs in the ESP32 Arduino core
Our sketches become tasks
Notes: Explain: Connect known Arduino habits to the ESP32's richer execution model.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Refresh the functions they will use immediately.

## Slide 9
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
09
Arduino code is a tiny contract with hardware
digitalRead
Button state
digitalWrite
LED or buzzer
analogRead
Potentiometer value
Serial
Debug messages
Notes: Explain: Keep this concrete: these calls are the workshop's sensor and actuator vocabulary.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: Which function reads a potentiometer?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show just enough syntax.

## Slide 10
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
10
Keep syntax small enough to debug live
arduino_refresher.ino
pinMode(LED_PIN, OUTPUT);
int button = digitalRead(BTN_PIN);
int knob = analogRead(POT_PIN);
analogWrite(LED_PIN, knob / 16);
Serial.println(button);
Pin modes first
Read inputs often
Print only what helps
Map ADC to output range
Notes: Explain: Do not teach all Arduino. Teach the subset needed for RTOS activities.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Now make the baseline blink.

## Slide 11
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
11
>> TASK ASSIGNED
HANDS_ON_LAB
Blink Baseline
OBJECTIVE
Make one LED blink with ordinary Arduino code.
STEPS
Create blink.ino
Use pinMode and digitalWrite
Use delay(500)
Confirm the LED toggles
EXPECTED OUTPUT
One LED blinks steadily.
CHALLENGE
Change the blink rate without rewiring.
HARDWARE
ESP32
LED
Resistor
Breadboard
Notes: Explain: Let teams work before explaining the complete answer. Objective: Make one LED blink with ordinary Arduino code.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 12
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
12
delay() is easy until anything else must happen
delay()
millis()
Simple to read
Blocks the whole loop
Hides missed button presses
Does not scale
Checks time without stopping
Lets other work continue
Builds the superloop pattern
Prepares timing thinking
Notes: Explain: Use the pain of delay as the first reason to think about scheduling.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign the millis version.

## Slide 13
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
13
>> TASK ASSIGNED
HANDS_ON_LAB
Blink with millis()
OBJECTIVE
Blink without blocking the loop.
STEPS
Store previousMillis
Compare now - previous
Toggle when interval expires
Print loop heartbeat
EXPECTED OUTPUT
LED blinks while Serial continues.
CHALLENGE
Add a button read without missing presses.
HARDWARE
ESP32
LED
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Blink without blocking the loop.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 14
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
14
MultiBlink is the first scheduling problem
LED A
500 ms
LED B
700 ms
LED C
1100 ms
Loop
keeps scanning
Notes: Explain: Multiple LEDs make students feel why manual timing gets busy.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Let them build MultiBlink before naming RTOS.

## Slide 15
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
15
>> TASK ASSIGNED
HANDS_ON_LAB
MultiBlink on one core
OBJECTIVE
Run two or more LEDs with different non-blocking intervals.
STEPS
Create multiblink.ino
Give each LED its own interval
Use separate previousMillis values
Observe independent blink rates
EXPECTED OUTPUT
LEDs blink independently.
CHALLENGE
Add a third LED cleanly.
HARDWARE
ESP32
2 LEDs
Resistors
Notes: Explain: Let teams work before explaining the complete answer. Objective: Run two or more LEDs with different non-blocking intervals.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 16
MODULE 00
ESP32_FREE_RTOS_WORKSHOP
16
ESP32 has two cores, but code still needs structure
Core 0
Core 1
Often handles system work
Can run pinned tasks
Not a magic fix
Often runs Arduino loop
Can run app work
Still shares resources
Notes: Explain: Introduce dual-core without pretending parallel hardware removes coordination problems.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign the dual-core experiment.

## Slide 17
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
17
>> TASK ASSIGNED
HANDS_ON_LAB
MultiBlink on both cores
OBJECTIVE
Pin blink tasks to different ESP32 cores and observe behavior.
STEPS
Print xPortGetCoreID()
Create two tasks
Pin one task to each core
Compare blink stability
EXPECTED OUTPUT
Serial shows two core IDs.
CHALLENGE
What happens if both tasks print too much?
HARDWARE
ESP32
2 LEDs
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Pin blink tasks to different ESP32 cores and observe behavior.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 18
MODULE 01
ESP32_FREE_RTOS_WORKSHOP
18
MODULE 01
Superloop
// the pattern every Arduino student already knows
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Superloop. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 19
MODULE 01
ESP32_FREE_RTOS_WORKSHOP
19
A superloop does every job in one long turn
01
Read
02
Decide
03
Display
04
Alert
05
Repeat
Notes: Explain: Name the pattern students have already used so it becomes inspectable.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show what happens when one step blocks.

## Slide 20
MODULE 01
ESP32_FREE_RTOS_WORKSHOP
20
One slow step makes the whole product feel slow
Button
fast
Sensor
ok
delay
blocks
LCD
late
Buzzer
late
Notes: Explain: Make blocking visible. The timeline is the simplest way to show a system getting stuck.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Compare superloop with FreeRTOS.

## Slide 21
MODULE 01
ESP32_FREE_RTOS_WORKSHOP
21
Superloop code grows by accident
superloop.ino
structured firmware
One function owns everything
Timing logic is scattered
Long delays break responsiveness
Hard to test one behavior
Jobs are separated
Timing belongs to tasks or timers
Events wake the right worker
Modules are easier to reason about
Notes: Explain: Position RTOS as a design tool, not a buzzword.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Make students diagnose blockers.

## Slide 22
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
22
>> TASK ASSIGNED
HANDS_ON_LAB
Find the blockers
OBJECTIVE
Mark where a loop-based sketch can miss an event.
STEPS
Run a blocking loop
Press the button during delay
Circle slow lines
Replace one delay with millis
EXPECTED OUTPUT
A list of blocking points.
CHALLENGE
Which line would fail first in a real product?
HARDWARE
Existing sketch
Serial Monitor
Button
Notes: Explain: Let teams work before explaining the complete answer. Objective: Mark where a loop-based sketch can miss an event.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 23
MODULE 02
ESP32_FREE_RTOS_WORKSHOP
23
MODULE 02
Need for RTOS
// when one loop is no longer enough
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Need for RTOS. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 24
MODULE 02
ESP32_FREE_RTOS_WORKSHOP
24
RTOS gives each job a place to run
Task
A named worker
Scheduler
Chooses who runs
Delay
Yields the CPU
Sync
Coordinates events
Notes: Explain: Introduce RTOS as a small operating discipline inside the microcontroller.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Separate concurrency from parallelism.

## Slide 25
MODULE 02
ESP32_FREE_RTOS_WORKSHOP
25
Concurrent does not always mean parallel
Concurrent
Parallel
Many jobs make progress
Can happen on one core
Scheduler switches between tasks
Jobs run at the same instant
Needs multiple cores
Still needs shared-resource rules
Notes: Explain: This avoids a common first-year misconception.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Define real-time carefully.

## Slide 26
MODULE 02
ESP32_FREE_RTOS_WORKSHOP
26
Real-time means predictable enough for the job
Deadline
When output must happen
Jitter
Variation in timing
Priority
Who matters first
Determinism
Behavior you can reason about
Notes: Explain: Keep real-time practical: not fastest, but predictable.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Open the FreeRTOS architecture.

## Slide 27
MODULE 02
ESP32_FREE_RTOS_WORKSHOP
27
FreeRTOS is a small set of rules and queues
01
Tasks
02
Scheduler
03
Kernel
04
IPC
05
Hardware
Notes: Explain: Show architecture at a distance before API names.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign a mental-model conversion.

## Slide 28
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
28
>> TASK ASSIGNED
HANDS_ON_LAB
Convert the mental model
OBJECTIVE
Rewrite one superloop behavior as named RTOS jobs.
STEPS
List every repeated job
Name each job as a task
Mark shared hardware
Mark events
EXPECTED OUTPUT
A task map for the sketch.
CHALLENGE
Which job should never block?
HARDWARE
Notebook
Marker
Existing sketch
Notes: Explain: Let teams work before explaining the complete answer. Objective: Rewrite one superloop behavior as named RTOS jobs.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 29
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
29
MODULE 03
Tasks
// independent work units
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Tasks. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 30
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
30
A task is just a function that keeps working
task_anatomy.cpp
void ledTask(void *param) {
while (1) {
digitalWrite(LED, !digitalRead(LED));
vTaskDelay(pdMS_TO_TICKS(500));
}
}
Function gets a void* parameter
while(1) keeps it alive
vTaskDelay yields
Never return accidentally
Notes: Explain: Make tasks less mysterious by showing they are ordinary functions with a loop.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show how a task is spawned.

## Slide 31
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
31
xTaskCreate names the worker and its budget
create_task.cpp
xTaskCreate(
ledTask, // function
"LED", // name
2048, // stack
NULL, // parameter
1, // priority
NULL // handle
);
Function
Name
Stack
Priority
Handle
Notes: Explain: Explain every argument visually; do not ask students to memorize it yet.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Place tasks on a lifecycle.

## Slide 32
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
32
Tasks move through a small lifecycle
01
Created
02
Ready
03
Running
04
Blocked
05
Deleted
Notes: Explain: The lifecycle unlocks later scheduling and debugging slides.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Zoom in on delay.

## Slide 33
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
33
vTaskDelay is a polite pause
delay()
vTaskDelay()
Blocks the Arduino loop
No RTOS awareness
Other loop work waits
Blocks only this task
Scheduler runs another task
Timing uses ticks
Notes: Explain: This is one of the most important early distinctions.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Bring in priority.

## Slide 34
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
34
Priority is a promise, not a decoration
Higher
Runs before lower ready tasks
Equal
Can time-slice
Blocked
Cannot run until unblocked
Wrong
Can starve other work
Notes: Explain: Warn against giving every task high priority.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign blink task.

## Slide 35
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
35
>> TASK ASSIGNED
HANDS_ON_LAB
Blink as a FreeRTOS task
OBJECTIVE
Move blink.ino into a task using vTaskDelay.
STEPS
Create ledTask
Call xTaskCreate in setup
Leave loop empty
Print task heartbeat
EXPECTED OUTPUT
LED blinks from a task.
CHALLENGE
Create a task handle and suspend it.
HARDWARE
ESP32
LED
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Move blink.ino into a task using vTaskDelay.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 36
MODULE 03
ESP32_FREE_RTOS_WORKSHOP
36
Suspend and resume are explicit control levers
01
Running
02
Suspend
03
Paused
04
Resume
05
Ready
Notes: Explain: The handwritten schedule includes suspend-resume. Teach it as a control tool, not a default pattern.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Let students wire it to a button.

## Slide 37
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
37
>> TASK ASSIGNED
HANDS_ON_LAB
Suspend and resume a task
OBJECTIVE
Use a button or Serial command to pause and resume blinking.
STEPS
Save the task handle
Call vTaskSuspend(handle)
Call vTaskResume(handle)
Print state changes
EXPECTED OUTPUT
Blink pauses and resumes on command.
CHALLENGE
Can another task still run while LED is suspended?
HARDWARE
ESP32
LED
Button
Notes: Explain: Let teams work before explaining the complete answer. Objective: Use a button or Serial command to pause and resume blinking.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 38
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
38
>> TASK ASSIGNED
HANDS_ON_LAB
MultiBlink with tasks
OBJECTIVE
Create two independent LED tasks with different delays.
STEPS
Create ledTaskA
Create ledTaskB
Use different intervals
Watch both tasks run
EXPECTED OUTPUT
Two task-driven blink rates.
CHALLENGE
Pin one task to each core.
HARDWARE
ESP32
2 LEDs
Resistors
Notes: Explain: Let teams work before explaining the complete answer. Objective: Create two independent LED tasks with different delays.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 39
MODULE 04
ESP32_FREE_RTOS_WORKSHOP
39
MODULE 04
Scheduling
// who gets the CPU next
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Scheduling. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 40
MODULE 04
ESP32_FREE_RTOS_WORKSHOP
40
The scheduler is the traffic controller
Task A
runs
Task B
ready
Task A
delays
Task B
runs
Idle
fills gaps
Notes: Explain: Use the traffic controller analogy so the scheduler feels concrete.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Connect it to task states.

## Slide 41
MODULE 04
ESP32_FREE_RTOS_WORKSHOP
41
Ready, running, blocked explains most timing bugs
01
Ready
02
Running
03
Blocked
04
Ready
Notes: Explain: Most FreeRTOS debugging starts by asking which state a task is in.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Layer priorities on top.

## Slide 42
MODULE 04
ESP32_FREE_RTOS_WORKSHOP
42
Priority decides first; time slicing decides ties
Priority 3
Runs first when ready
Priority 2
Runs when higher priority work blocks
Priority 1
Background or slow work
Same priority
Can share time slices
Notes: Explain: Keep the policy simple before discussing deeper scheduling internals.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Relate this back to ESP32 cores.

## Slide 43
MODULE 04
ESP32_FREE_RTOS_WORKSHOP
43
Core affinity is useful after the task model is clear
Pinned
Task stays on a chosen core
Unpinned
RTOS may choose
Shared
Resources still need protection
Debug
Print core ID carefully
Notes: Explain: Teach dual-core as an extension of scheduling, not the first solution.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign scheduling observation.

## Slide 44
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
44
>> TASK ASSIGNED
HANDS_ON_LAB
Observe scheduling
OBJECTIVE
Print task names, priorities, delays, and core IDs.
STEPS
Create three tasks
Use different priorities
Add vTaskDelay
Log core ID and tick count
EXPECTED OUTPUT
Serial shows interleaved execution.
CHALLENGE
Make a low-priority task starve, then fix it.
HARDWARE
ESP32
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Print task names, priorities, delays, and core IDs.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 45
MODULE 05
ESP32_FREE_RTOS_WORKSHOP
45
MODULE 05
Queues
// data moves without global chaos
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Queues. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 46
MODULE 05
ESP32_FREE_RTOS_WORKSHOP
46
A queue lets tasks hand off data safely
01
Producer
02
Queue
03
Consumer
04
Action
Notes: Explain: Queues solve data transfer between independent jobs.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show API at a tiny scale.

## Slide 47
MODULE 05
ESP32_FREE_RTOS_WORKSHOP
47
Queue APIs are about ownership and waiting
queue_core.cpp
QueueHandle_t q;
q = xQueueCreate(5, sizeof(int));
xQueueSend(q, &value, 0);
if (xQueueReceive(q, &value, portMAX_DELAY)) {
updateDisplay(value);
}
Create storage
Send a copy
Receive into a variable
Choose timeout intentionally
Notes: Explain: Point out that queues copy data by size.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Build the three-task picture.

## Slide 48
MODULE 05
ESP32_FREE_RTOS_WORKSHOP
48
Three tasks can behave like one clean product
01
Read knob
02
Send value
03
Control task
04
LCD task
05
Alert task
Notes: Explain: The proposal's event-management activity becomes a concrete architecture.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Warn about queue misuse.

## Slide 49
MODULE 05
ESP32_FREE_RTOS_WORKSHOP
49
Queue mistakes usually look like timing bugs
Wrong size
Data corrupts or truncates
No timeout
Task waits forever
Full queue
New data is dropped
Too much data
Use pointers carefully
Notes: Explain: Give debugging warnings before the activity.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign the queue run.

## Slide 50
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
50
>> TASK ASSIGNED
HANDS_ON_LAB
Queue run
OBJECTIVE
Send button or potentiometer values from one task to another.
STEPS
Create a queue
Producer reads ADC
Consumer receives value
Print filtered result
EXPECTED OUTPUT
Values move through the queue.
CHALLENGE
Change queue length and observe lag.
HARDWARE
ESP32
Potentiometer
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Send button or potentiometer values from one task to another.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 51
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
51
>> TASK ASSIGNED
HANDS_ON_LAB
Three-task queue
OBJECTIVE
Build producer, processor, and display tasks connected by a queue.
STEPS
Producer reads input
Processor maps value
Display task owns LCD
Queue carries messages
EXPECTED OUTPUT
LCD updates from queued data.
CHALLENGE
Add a warning threshold.
HARDWARE
ESP32
Potentiometer
LCD
Notes: Explain: Let teams work before explaining the complete answer. Objective: Build producer, processor, and display tasks connected by a queue.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 52
MODULE 06
ESP32_FREE_RTOS_WORKSHOP
52
MODULE 06
Semaphores
// event signals between tasks
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Semaphores. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A doorbell or event buzzer: one press wakes the right worker.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 53
MODULE 06
ESP32_FREE_RTOS_WORKSHOP
53
A semaphore is a signal, not a data packet
Queue
Semaphore
Carries data
Can store many messages
Consumer reads values
Carries permission or event
Often just yes/no
Consumer wakes up
Notes: Explain: Separate queues from semaphores before students blend them.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A doorbell or event buzzer: one press wakes the right worker.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show button to LCD.

## Slide 54
MODULE 06
ESP32_FREE_RTOS_WORKSHOP
54
Button events can wake exactly the right task
01
Button task
02
Give
03
Semaphore
04
Take
05
Alert task
Notes: Explain: Use the smart notification system from the proposal.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Binary versus counting.

## Slide 55
MODULE 06
ESP32_FREE_RTOS_WORKSHOP
55
Binary and counting semaphores answer different questions
Binary
Counting
Did an event happen?
0 or 1 token
Button press signal
How many events/resources?
0 to N tokens
Buffered events or slots
Notes: Explain: Keep the difference visual and practical.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A doorbell or event buzzer: one press wakes the right worker.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign toggle semaphore.

## Slide 56
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
56
>> TASK ASSIGNED
HANDS_ON_LAB
Semaphore toggle
OBJECTIVE
Signal an LED or buzzer task from a button task.
STEPS
Create binary semaphore
Button task gives it
Alert task takes it
Toggle output
EXPECTED OUTPUT
Output changes only after the signal.
CHALLENGE
Debounce the button without blocking.
HARDWARE
ESP32
Button
LED
Buzzer
Notes: Explain: Let teams work before explaining the complete answer. Objective: Signal an LED or buzzer task from a button task.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A doorbell or event buzzer: one press wakes the right worker.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 57
DAY 1
ESP32_FREE_RTOS_WORKSHOP
57
Day 1 mini-project ties the first tools together
Mode switching with tasks, queues, semaphores, display, LED, and buzzer.
01
Input
02
Mode queue
03
Controller
04
LCD
05
Feedback
Notes: Explain: This is the proposal mini-project, adapted to the handwritten Day 1 flow.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Close Day 1 with a short synthesis.

## Slide 58
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
58
>> TASK ASSIGNED
HANDS_ON_LAB
Day 1 mini-project
OBJECTIVE
Build a multi-mode embedded system with visible feedback.
STEPS
Input task detects mode change
Queue sends selected mode
Display task updates LCD
Semaphore triggers alert
EXPECTED OUTPUT
Standby, monitor, and alert modes work.
CHALLENGE
Add a fourth mode without rewriting every task.
HARDWARE
ESP32
LCD
Buttons
LEDs
Buzzer
Notes: Explain: Let teams work before explaining the complete answer. Objective: Build a multi-mode embedded system with visible feedback.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 59
DAY 1
ESP32_FREE_RTOS_WORKSHOP
59
By the end of Day 1, the loop has become a team
Tasks
Jobs are named
Scheduler
CPU time is shared
Queues
Data moves safely
Semaphores
Events wake tasks
Notes: Explain: Summarize without adding new material. This is a mental checkpoint.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Day 2 starts with timed work that does not need a full task.

## Slide 60
DAY 2 / MODULE 07
ESP32_FREE_RTOS_WORKSHOP
60
DAY 2 / MODULE 07
Software Timers
// timed callbacks without extra task clutter
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Software Timers. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: An alarm clock that calls a callback at a fixed time.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 61
MODULE 07
ESP32_FREE_RTOS_WORKSHOP
61
A software timer runs a callback later
01
Create
02
Start
03
Expire
04
Callback
05
Repeat
Notes: Explain: Introduce timers as lightweight time-based triggers.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: An alarm clock that calls a callback at a fixed time.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show the timer service task.

## Slide 62
MODULE 07
ESP32_FREE_RTOS_WORKSHOP
62
Timer callbacks run inside the timer service task
Callback
Keep it short
No blocking
Do not wait forever
One-shot
Runs once
Auto-reload
Runs repeatedly
Notes: Explain: This prevents students from putting long work inside a timer callback.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: An alarm clock that calls a callback at a fixed time.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign timer blink.

## Slide 63
MODULE 07
ESP32_FREE_RTOS_WORKSHOP
63
Timers are perfect for periodic small signals
timer_blink.cpp
TimerHandle_t t;
void blinkCb(TimerHandle_t xTimer) {
digitalWrite(LED, !digitalRead(LED));
}
t = xTimerCreate("blink", pdMS_TO_TICKS(500),
pdTRUE, NULL, blinkCb);
xTimerStart(t, 0);
Callback toggles LED
Auto-reload repeats
No dedicated blink task
Keep callback tiny
Notes: Explain: Show the core API for software timers.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: An alarm clock that calls a callback at a fixed time.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Hands-on timer blink.

## Slide 64
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
64
>> TASK ASSIGNED
HANDS_ON_LAB
Blink using timers
OBJECTIVE
Recreate blink and multiblink with software timers.
STEPS
Create one auto-reload timer
Toggle LED in callback
Add second timer at 200 ms
Compare with task-based blink
EXPECTED OUTPUT
LEDs blink without blink tasks.
CHALLENGE
When is a task better than a timer?
HARDWARE
ESP32
2 LEDs
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Recreate blink and multiblink with software timers.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: An alarm clock that calls a callback at a fixed time.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 65
DAY 2 / MODULE 08
ESP32_FREE_RTOS_WORKSHOP
65
DAY 2 / MODULE 08
Mutex
// shared hardware needs ownership
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Mutex. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: One key for the LCD: only the task holding the key can write.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 66
MODULE 08
ESP32_FREE_RTOS_WORKSHOP
66
Shared resources fail when everyone writes at once
Task A
LCD line 1
Task B
LCD line 2
Task A
overwrites
Display
garbled
Notes: Explain: Mutex is entirely Day 2 per the latest plan.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Introduce the key analogy.

## Slide 67
MODULE 08
ESP32_FREE_RTOS_WORKSHOP
67
A mutex is the key to a shared device
01
Take key
02
Use LCD
03
Release key
04
Next task
Notes: Explain: Make ownership visible. The shared LCD is the best workshop example.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: One key for the LCD: only the task holding the key can write.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Mention priority inversion briefly.

## Slide 68
MODULE 08
ESP32_FREE_RTOS_WORKSHOP
68
Priority inversion is a scheduling surprise
Low task
Holds the mutex
High task
Waits for resource
Medium task
Can delay release
Inheritance
FreeRTOS can help
Notes: Explain: Give the concept, not a graduate lecture. It is a cautionary tale.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign the LCD mutex lab.

## Slide 69
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
69
>> TASK ASSIGNED
HANDS_ON_LAB
Protect the LCD with a mutex
OBJECTIVE
Let multiple tasks update the LCD without corrupting output.
STEPS
Create mutex
Each task takes before LCD write
Release after write
Stress with fast updates
EXPECTED OUTPUT
LCD updates stay readable.
CHALLENGE
What happens if a task forgets to give the mutex?
HARDWARE
ESP32
I2C LCD
2 tasks
Notes: Explain: Let teams work before explaining the complete answer. Objective: Let multiple tasks update the LCD without corrupting output.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: One key for the LCD: only the task holding the key can write.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 70
DAY 2 / MODULE 09
ESP32_FREE_RTOS_WORKSHOP
70
DAY 2 / MODULE 09
Memory Management
// every task needs a stack
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Memory Management. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A backpack with limited space: each task needs enough stack but not the whole bag.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 71
MODULE 09
ESP32_FREE_RTOS_WORKSHOP
71
Stack and heap are different budgets
Stack
Heap
Private space for one task
Local variables and calls
Too small causes crashes
Shared allocation pool
Queues, tasks, dynamic objects
Fragmentation can hurt
Notes: Explain: Use memory as a practical debugging topic.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show stack sizing.

## Slide 72
MODULE 09
ESP32_FREE_RTOS_WORKSHOP
72
Each task stack should be enough, not enormous
Task: display stack
Task: sensor stack
Task: alert stack
Free heap for system objects
Notes: Explain: Make memory visible as a set of budgets.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show the monitoring API.

## Slide 73
MODULE 09
ESP32_FREE_RTOS_WORKSHOP
73
Stack high-water mark tells you the spare margin
stack_check.cpp
UBaseType_t left;
left = uxTaskGetStackHighWaterMark(NULL);
Serial.print("stack words left: ");
Serial.println(left);
Call inside the task
Low number means danger
Check after real workload
Do not guess stack sizes
Notes: Explain: Teach students one concrete memory measurement.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign stack experiment.

## Slide 74
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
74
>> TASK ASSIGNED
HANDS_ON_LAB
Stack size experiment
OBJECTIVE
Create tasks with different stack sizes and observe behavior.
STEPS
Create two tasks
Give one a tiny stack
Print high-water mark
Increase until stable
EXPECTED OUTPUT
Students see stack margin change.
CHALLENGE
Add local arrays and observe impact.
HARDWARE
ESP32
Serial Monitor
Notes: Explain: Let teams work before explaining the complete answer. Objective: Create tasks with different stack sizes and observe behavior.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 75
DAY 2 / MODULE 10
ESP32_FREE_RTOS_WORKSHOP
75
DAY 2 / MODULE 10
Interrupts
// urgent events enter safely
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Interrupts. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A fire alarm: it interrupts normal work but should hand off quickly.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 76
MODULE 10
ESP32_FREE_RTOS_WORKSHOP
76
An ISR should be fast and hand off work
01
Pin edge
02
ISR
03
Give signal
04
Task wakes
05
Handle event
Notes: Explain: Interrupts are emergency entry points, not a place to do full work.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show ISR-safe APIs.

## Slide 77
MODULE 10
ESP32_FREE_RTOS_WORKSHOP
77
ISR-safe calls use the FromISR family
button_isr.cpp
void IRAM_ATTR buttonISR() {
BaseType_t wake = pdFALSE;
xSemaphoreGiveFromISR(alertSem, &wake);
portYIELD_FROM_ISR(wake);
}
Keep ISR tiny
Use FromISR APIs
Request yield if needed
Do the real work in a task
Notes: Explain: Focus on the safe handoff pattern.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign emergency alert.

## Slide 78
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
78
>> TASK ASSIGNED
HANDS_ON_LAB
Emergency interrupt alert
OBJECTIVE
Use a button interrupt to trigger an alert task.
STEPS
Attach interrupt to button
Give semaphore from ISR
Alert task takes semaphore
Blink or buzz emergency pattern
EXPECTED OUTPUT
Emergency alert triggers immediately.
CHALLENGE
Add debounce outside the ISR.
HARDWARE
ESP32
Button
LED
Buzzer
Notes: Explain: Let teams work before explaining the complete answer. Objective: Use a button interrupt to trigger an alert task.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A fire alarm: it interrupts normal work but should hand off quickly.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 79
DAY 2 / MODULE 11
ESP32_FREE_RTOS_WORKSHOP
79
DAY 2 / MODULE 11
Task Notifications
// fast direct signals
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Task Notifications. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A direct phone ping to one task instead of posting a public message.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 80
MODULE 11
ESP32_FREE_RTOS_WORKSHOP
80
A task notification is a direct signal to one task
01
Producer
02
Notify
03
Target task
04
Wake
05
Act
Notes: Explain: Notifications are lightweight, but they target one task.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A direct phone ping to one task instead of posting a public message.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Compare with queue and semaphore.

## Slide 81
MODULE 11
ESP32_FREE_RTOS_WORKSHOP
81
Choose the lightest communication that fits
Queue
Use when you must send data
Semaphore
Use when you need an event token
Mutex
Use when a shared resource needs ownership
Notification
Use for fast direct task signalling
Notes: Explain: This slide helps students select mechanisms instead of collecting APIs.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Assign the LCD notification lab.

## Slide 82
MODULE 11
ESP32_FREE_RTOS_WORKSHOP
82
Notifications can update a display without a queue
notify_lcd.cpp
xTaskNotifyGive(displayTaskHandle);
ulTaskNotifyTake(pdTRUE, portMAX_DELAY);
updateDisplay();
Direct to one task
Very low overhead
Can count events
Not for complex data
Notes: Explain: Show the essential pattern in four lines.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A restaurant order queue: orders arrive, the kitchen consumes them in a controlled way.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Hands-on notification activity.

## Slide 83
TASK ASSIGNED // HANDS-ON
ESP32_FREE_RTOS_WORKSHOP
83
>> TASK ASSIGNED
HANDS_ON_LAB
Notify the LCD task
OBJECTIVE
Trigger LCD updates through direct task notifications.
STEPS
Save display task handle
Notify from input task
Display task waits
Update only when notified
EXPECTED OUTPUT
LCD updates on direct notification.
CHALLENGE
Replace semaphore with notification and compare code.
HARDWARE
ESP32
I2C LCD
Button
Notes: Explain: Let teams work before explaining the complete answer. Objective: Trigger LCD updates through direct task notifications.
Analogy: Like debugging a tiny lab instrument: change one variable and observe the output.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do you expect to see before uploading?
Common mistake: Common mistake: wiring and pin numbers are confused with RTOS logic. Separate hardware debugging from code debugging.
Animation suggestion: Keep the activity title fixed; reveal steps as the room catches up.
Transition suggestion: After the activity, ask one group to describe the symptom they saw.

## Slide 84
FINAL BUILD
ESP32_FREE_RTOS_WORKSHOP
84
FINAL BUILD
Integrated FreeRTOS Application
// every concept earns its place
NEXT_MODULE
Notes: Explain: Use this as a clean reset before Integrated FreeRTOS Application. Frame what students are about to build.
Analogy: A workshop module is like enabling the next subsystem in firmware.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What do we already know that will help here?
Common mistake: Do not dive into syntax on the divider slide.
Animation suggestion: Use a simple wipe or fade.
Transition suggestion: Start the next slide with the simplest mental model.

## Slide 85
FINAL BUILD
ESP32_FREE_RTOS_WORKSHOP
85
The final app is a network of small jobs
01
Sensors
02
Queue
03
Controller
04
LCD mutex
05
Alerts
Notes: Explain: Tie together all modules into the final monitoring and control system.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Show build checkpoints.

## Slide 86
FINAL BUILD
ESP32_FREE_RTOS_WORKSHOP
86
Build the final project in checkpoints
1
Tasks alive
2
Data queued
3
LCD protected
4
ISR alert
5
Demo stable
Notes: Explain: Give a build sequence that prevents students from trying everything at once.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Give the demo rubric.

## Slide 87
FINAL BUILD
ESP32_FREE_RTOS_WORKSHOP
87
A good demo proves behavior, not just code
Stable
No random resets
Responsive
Button and ISR react
Readable
LCD stays clean
Explainable
Team can justify each primitive
Notes: Explain: Set expectations for teams before final demos.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Summarize the learning outcomes.

## Slide 88
SUMMARY
ESP32_FREE_RTOS_WORKSHOP
88
Students now have a firmware design vocabulary
Tasks
Separate responsibilities
Scheduler
Predict CPU sharing
IPC
Move data and events
Protection
Own shared hardware
Integration
Build real systems
Notes: Explain: Match the proposal learning outcomes in student-friendly language.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: What would break first if this ran inside one long loop?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: End with one simple close.

## Slide 89
THANK YOU
ESP32_FREE_RTOS_WORKSHOP
89
Your loop is no longer alone
Next step: make the final build reliable enough to explain under pressure.
01
Observe
02
Separate
03
Schedule
04
Communicate
05
Protect
Notes: Explain: Close by reinforcing confidence and the system-thinking arc.
Analogy: A small embedded system is like a tiny team: each part needs a clear job and a way to coordinate.
Real-world example: A smartwatch, drone, or car dashboard where sensing, display, alerts, and input happen together.
Ask students: Which FreeRTOS primitive would you reach for first in your own project?
Common mistake: Students may memorize API names before understanding the timing or ownership problem.
Animation suggestion: Reveal the diagram or cards one step at a time.
Transition suggestion: Invite questions and final demos.